## Slide 1
1. System Diagram
Software Documentation – Team M112
Analogue Pins |  | 
Pin | Name | Function
A0 | Left Line sensor | Connect the 4 line sensors to analogue input to detect the black, white colors on the table. Use as the input states for line follower algorithm. 4 sensors give us enough states and great flexibility to handle with different situations.
A1 | Middle LS1 | 
A2 | Middle LS2 | 
A3 | Right LS | 
A4 | LDR Sensor Red | Read values from LDR sensors and take the difference. Two sensor values allow us to calibrate according to different daylight condition and eliminate its influence.
A5 | LDR Sensor Blue | 
Digital Pins | 
Pin | Name
2 | Green LED
3 | Amber LED
4 | Red LED
5 | Start Button
6 | US Sensor Distance
12 | US Sensor echo pin
13 | US Sensor trig pin
Motor Shield | 
Motor 1 | Take the speed and direction (1 forward, 0 backward) as input
Motor 2 | 
Start button
Button state == 1
Robot Initialization
Line follower
Read 2 color inputs (A4, A5)
Calibration color value
Receive 4 line sensor value inputs (input A0, A1, A2, A3)
Receive echo sound wave (input 12)
Amber LED flash (output 3)
Set motor move forward (M1, M2)
Send sound wave from trig pin (output 13)
Set motor movement (M1, M2)
Fruit Detection & Analysis
Received Boolean, whether fruit is detected within 5cm (input 12)
Read 2 color inputs and take difference (input A4, A5)
Amber LED light up (output 3)
Ripe or Unripe, set which LED output to be on (output 2, 4)
Fruit Handling
Motor movement (M1, M2)

## Slide 2
Overall system
A0
A1
A2
A3
A4
Analogue input
Digital input (2, 3, 4, 5 )
Ultrasonic sensor input (6, 12, 13)
M1, M2 motor output
LED output
A5

## Slide 3
2. Code Structures & Algorithms
State 0:
Robot Idle
State 1
Ultrasound Detection
Button pressed
Button not pressed
State 2
Line-Following Algorithm
Fruit detected
State 3
Fruit Analysis (Colour Detector)
Fruit not detected
Fruit is unripe
Fruit is ripe
State 4
Handle Ripe Fruit (Collect)
State 3
Handle Unripe Fruit (Avoid)
Number of fruits detected == 6
Number of fruits detected != 6
State 6
Line-Following Algorithm (Homebound)
Source Code available at:
https://gitlab.com/talpha/idp_m112_2020/-/blob/master/greedy_algorithm/greedy_algorithm.ino
Overall Structure (Finite-state Automaton Design)
Line-Following Algorithm (Lines 273-353)
Colour Detector Algorithm (Lines 153-179)
Calls readLineSensorArray
Calls readLineSensor on A0-A3, which
reads analog input, compares the input value to a pre-defined threshold value, and returns an integer of 1 or 0
Concatenates the 4 integers returned by 4 readLineSensor calls into a single string (e.g. “1111”)
Calls activateLineFollower0
Set motor speeds based on String output (16 states from 0000 to 1111)
Calibration step Save the difference in readings for both sensors (saved as var calibrate_colour) under the same light conditions
Read sensorValueRed
Read sensorValueBlue
Fruit is ripe
Fruit is unripe
Save difference in reading as var difference_colour
difference_colour > calibrate_colour
difference_colour < calibrate_colour